1605R#show run

Building configuration...

Current configuration : 1622 bytes

!

version 12.2

service timestamps debug uptime

service timestamps log uptime

service password-encryption

!

hostname 1605R

!

enable password 7 121A0C041104

!

ip subnet-zero

ip name-server 213.154.225.35

ip dhcp excluded-address 172.16.1.1 172.16.1.99

!

ip dhcp pool DHCP-local

network 172.16.1.0 255.255.255.0

default-router 172.16.1.254

!

isdn switch-type basic-net3

!

interface Ethernet0

description connected to EthernetLAN

ip address 172.16.1.254 255.255.255.0

ip nat inside

!

interface Ethernet1

description connected to WIFI

ip address dhcp

ip nat outside

!

interface BRI0

description backup ISDN to KPN

no ip address

ip nat outside

encapsulation ppp

shutdown

dialer rotary-group 1

dialer-group 1

isdn switch-type basic-net3

no cdp enable

!

interface Dialer1

description connected to Internet

ip address negotiated

ip nat outside

encapsulation ppp

no ip split-horizon

dialer in-band

dialer idle-timeout 180

dialer string 0676001505

dialer hold-queue 10

dialer-group 1

no cdp enable

ppp authentication chap pap callin

ppp chap hostname **********

ppp chap password xxxxxxxxxx

ppp pap sent-username ********** password xxxxxxxxxx

!

ip nat inside source list 1 interface Ethernet1 overload

ip classless

ip route 0.0.0.0 0.0.0.0 213.136.27.129

no ip http server

!

!

access-list 1 permit 172.16.1.0 0.0.0.255

dialer-list 1 protocol ip permit

snmp-server community public RO

snmp-server enable traps tty

!

line con 0

exec-timeout 0 0

password 7 121A0C041104

login

line vty 0 4

access-class 1 in

password 7 13061E010803

login

!

end

1605R#

1605R#show ver

Cisco Internetwork Operating System Software

IOS (tm) 1600 Software (C1600-OY-M), Version 12.2(11)T8,  RELEASE SOFTWARE (fc1)

TAC Support: http://www.cisco.com/tac

Copyright (c) 1986-2003 by cisco Systems, Inc.

Compiled Wed 26-Mar-03 16:24 by hqluong

Image text-base: 0x02005000, data-base: 0x02756DF8

ROM: System Bootstrap, Version 12.0(3)T, RELEASE SOFTWARE (fc1)

ROM: 1600 Software (C1600-RBOOT-R), Version 12.0(3)T,  RELEASE SOFTWARE (fc1)

1605R uptime is 8 hours, 59 minutes

System returned to ROM by power-on

System image file is "flash:c1600-oy-mz.122-11.T8.bin"

cisco 1605 (68360) processor (revision C) with 11776K/512K bytes of memory.

Processor board ID 26403857, with hardware revision 00000004

Bridging software.

X.25 software, Version 3.0.0.

Basic Rate ISDN software, Version 1.1.

2 Ethernet/IEEE 802.3 interface(s)

1 ISDN Basic Rate interface(s)

System/IO memory with parity disabled

8192K bytes of DRAM onboard 4096K bytes of DRAM on SIMM

System running from RAM

7K bytes of non-volatile configuration memory.

4096K bytes of processor board PCMCIA flash (Read/Write)

Configuration register is 0x2102